## Slide 1
WATER & WASTEWATER PROCESS ENGINEERING
WaterSim Pro
A web-based simulation platform for designing, costing and operating water purification and wastewater treatment plants.
Draw the plant · Simulate the process · See the cost · Prove compliance
React 18 + Vite
Node.js + Express
PostgreSQL
WebSocket live
Python reporting
WaterSim Pro
1
Notes: Opening line: "WaterSim Pro is a browser-based process simulator for water and wastewater treatment plants." Everything a process engineer would otherwise do across a desktop simulator, a costing spreadsheet and a permit PDF happens in one place. Runs on React, Node and PostgreSQL, with a WebSocket channel for live data and a Python layer for reporting.

## Slide 2
CONTENTS
What this deck covers
Three parts: what the product is, how it is built, and how work flows through it.
01
Introduction
The problem, what WaterSim Pro does, and who uses it.
02
Architecture
System layers, technology stack and the data model.
03
The Flows
Ten end-to-end journeys, from login to a signed-off report.
04
Engineering
Performance, security, testing and deployment.
In one line: an engineer draws a treatment train on a canvas, WaterSim Pro solves the mass balance, prices the plant, checks it against the discharge permit, and turns the result into a report anyone can read.
WaterSim Pro
Contents
2
Notes: Four parts. Introduction is the product and its users. Architecture is how it is built. The Flows is the bulk of the deck — ten journeys through the system. Engineering is the non-functional work. If the audience is technical, spend the time in parts 2 and 3.

## Slide 3
WHY IT EXISTS
Designing a treatment plant is slow, siloed and hard to check
Process design today is spread across desktop simulators, spreadsheets and PDFs — none of which talk to each other.
Desktop-only tools
Licences are per seat and per machine. Nobody outside the process team can open the model, so review happens by emailing screenshots.
Spreadsheet costing
CAPEX and OPEX live in a separate workbook from the mass balance. Change a basin volume and the cost silently goes stale.
Compliance checked by hand
Effluent limits are re-typed from the permit into the model each time, so a missed limit is only found at the review meeting.
No link to the real plant
The design model and the running plant are two different worlds — the simulation is never confronted with live SCADA data.
WaterSim Pro puts all four in one browser tab — one model, one number, one source of truth.
WaterSim Pro
Introduction
3
Notes: Frame the pain before the product. Four real problems, and they compound: because the tools are separate, costing goes stale, compliance is manual, and the live plant is invisible to the model. The closing line is the whole pitch — one model, one number, one source of truth.

## Slide 4
THE PRODUCT
What WaterSim Pro does
Six capabilities, all reachable from the same flowsheet.
Visual flowsheet canvas
Drag 26 unit operations onto a drawing sheet, wire them together, set parameters per node. Live values animate on the symbols.
Process simulation
A steady-state solver plus a 24-hour dynamic solver, with true branching, mixing and RAS/WAS recycle loops.
Cost estimation
Per-unit CAPEX from sizing correlations, five OPEX categories, annualised capital and a levelised cost of water.
Permit compliance
Organisation-level effluent permit templates; every run is scored pass or fail against the active limits.
Live plant data & alarms
Bind canvas parameters to PLC tags over Modbus, OPC UA, S7 or EtherNet/IP; raise alarms on limits and keep an event history.
Reporting & collaboration
PDF, Excel and CSV exports, plain-language summaries, scenario comparison, and multi-user editing with presence.
WaterSim Pro
Introduction
4
Notes: Six capabilities. The key point is the last clause of the subtitle: all six hang off the same flowsheet. You do not re-enter the plant in a costing tool or a compliance tool.

## Slide 5
USERS & ACCESS
Four roles, each one inheriting the one below
Access control is hierarchical: a route guarded for engineers also admits admins.
Viewer
Reads projects, flowsheets and reports in their organisation.
Operator
Everything a viewer can do, plus running simulations on existing flowsheets.
Engineer
Creates and edits projects, flowsheets, unit costs, permits and alarm rules.
Admin
Full control: user management, organisation settings and every admin endpoint.
ISOLATION MODEL
Organisation
Every user, project, flowsheet, run, permit and alarm belongs to exactly one organisation.
Query scoping
Every database read is filtered by the organisation id carried in the JWT — cross-tenant access is not expressible.
Audit trail
Privileged actions are written to an audit_logs table with actor, action and target.
WaterSim Pro
Introduction
5
Notes: Hierarchical roles — that matters because it means permissions are declared once and inherited, not copied. The isolation model below is the multi-tenancy story: the organisation id comes from the verified token, so cross-tenant reads are not expressible in the query layer at all.

## Slide 6
PART 02
Architecture
How the system is put together — the layers, the stack and the data it keeps.
System layers
Technology stack
Data model
WaterSim Pro
6
Notes: Transition slide. "Now how it is actually built."

## Slide 7
ARCHITECTURE
The system in four layers
A React single-page app, an Express API, a PostgreSQL store, and two side channels for heavy work and live data.
Browser
React 18 SPA, code-split per route
Canvas (React Flow)
Dashboard & Projects
Reports & Comparison
Alarms & Admin
Live charts (Recharts)
HTTPS /api/v1 · JWT bearer · WebSocket
API
Express, 12 routers, 73 endpoints
Auth & RBAC
Projects & Flowsheets
Simulate & Reports
PLC & Alarms
Admin & Permits
Engines
Off the request path for heavy work
Worker threads (solver)
Cost estimator (CAPEX/OPEX)
Python reports (PDF/Excel)
PLC poller (500 ms tick)
Alarm evaluator (state machine)
Data
PostgreSQL 14+, 8 versioned migrations
Organisations & users
Projects & flowsheets
Simulation runs & saved reports
PLC connections & bindings
Alarm rules, events, audit
WaterSim Pro
Architecture
7
Notes: Read it top to bottom. The browser talks to one versioned API. The API delegates anything heavy to the Engines layer — worker threads, Python child processes, the PLC poller — so the request path stays fast. Everything durable lands in PostgreSQL under versioned migrations.

## Slide 8
ARCHITECTURE
Technology stack
A single npm-workspaces monorepo: one lockfile, two workspaces, one deployment pipeline.
CLIENT
Frontend
React 18, Vite 5, Tailwind CSS, React Router 6
State & data
TanStack Query (server state), Zustand (live canvas store)
Canvas
React Flow 11 — nodes, edges, custom symbols and stream edges
Charts
Recharts — live dock, dynamic-run time series, comparisons
Icons & a11y
lucide-react, ARIA live regions, skip links, focus traps
SERVER
Backend
Node.js 18+, Express 4, worker_threads for the solver
Database
PostgreSQL 14+ via pg, versioned JS migrations
Realtime
ws — WebSocket rooms keyed by flowsheet
Security
jsonwebtoken, bcryptjs, helmet, express-rate-limit, express-validator
Reporting
Python — reportlab (PDF), matplotlib (charts), openpyxl (Excel)
Tooling & operations: ESLint + Prettier · Jest (API) + Vitest (UI) + Playwright (E2E) · GitHub Actions CI/CD · Docker Compose and Kubernetes · Prometheus metrics + Winston logs
WaterSim Pro
Architecture
8
Notes: Nothing exotic. Worth calling out: React Flow for the canvas, worker_threads for the solver, and Python for reporting because reportlab and openpyxl are simply better than the Node equivalents. One lockfile across both workspaces keeps the Docker builds honest.

## Slide 9
ARCHITECTURE
The data model
Sixteen tables in five groups. Everything hangs off the organisation.
Tenancy & identity
organisations
users
refresh_tokens
audit_logs
Who you are, which organisation you belong to, and what you did.
Design
projects
project_members
flowsheets
flowsheet_snapshots
A project holds flowsheets; a snapshot is a read-only frozen version.
Results
simulation_runs
saved_reports
permit_templates
Every run keeps its config, results, cost breakdown and compliance verdict.
Live data
plc_connections
plc_bindings
A connection is a device; a binding maps one tag to one canvas parameter.
Alarms
alarm_rules
alarm_events
A rule is a limit on a validated target; an event is a breach with a lifecycle.
Schema changes ship as numbered, idempotent migrations (001 … 008) applied by "npm run db:migrate" before every rollout — never by hand.
WaterSim Pro
Architecture
9
Notes: Sixteen tables, five groups. If someone asks "where does X live", this is the slide. The bottom line is the operational discipline: migrations are numbered and applied by the pipeline, never by hand on a running database.

## Slide 10
PART 03
The Flows
How work actually moves through the platform — ten journeys, from the login screen to a signed-off report.
The end-to-end journey
Auth · Canvas · Simulation
Cost · Compliance · Reports
PLC · Alarms · Collaboration
WaterSim Pro
10
Notes: Transition. This is the longest part of the deck — say so, and offer to skip any flow the audience does not care about.

## Slide 11
THE CORE FLOW
The end-to-end journey
Seven steps take an engineer from a blank screen to a report a regulator can read.
Sign in
Create project
Draw flowsheet
Set parameters
Run simulation
Read results
Export report
1
Sign in
Email and password are exchanged for an access token plus a refresh cookie. Its organisation scopes everything that follows.
2
Create a project
A project is the container: a plant, a study or a tender. It carries its own unit-cost overrides and its own members.
3
Draw the flowsheet
Drag unit operations onto the canvas and wire them. Edges carry a stream role — effluent, RAS, WAS, sludge, permeate.
4
Set parameters
Select a node and edit its parameters in the side panel. Edits auto-save and broadcast to co-editors live.
5
Run the simulation
Choose steady-state, dynamic or batch. The solver runs in a worker thread, so a heavy flowsheet never blocks the API.
6
Read the results
Stream values land on the canvas, cost and permit verdict fill the summary panel, and a breached limit raises an alarm.
7
Export the report
A PDF engineering report, a multi-sheet Excel workbook or CSV — plus a plain-language summary for non-engineers.
WaterSim Pro
The Flows
11
Notes: The spine of the product. Walk the chevrons first, then the detail. If you only have five minutes for the whole deck, present this slide and slide 4.

## Slide 12
FLOW 01
Authentication and multi-tenancy
Two tokens with different lifetimes: a short access token in memory, a long refresh token in an httpOnly cookie.
Register
POST /auth/register creates the organisation and its first admin user.
Login
POST /auth/login returns an access token in JSON and sets the refresh token as an httpOnly cookie.
Call the API
Every protected request carries an Authorization: Bearer header. RBAC runs after that.
Refresh
On 401 the client calls POST /auth/refresh — a new access token, a rotated cookie.
Logout
POST /auth/logout revokes the refresh token server-side and clears the cookie.
WHAT PROTECTS IT
Password storage
bcrypt hashes only — the hash never leaves the model layer and is stripped from every response.
Token rotation
Refresh tokens are single-use and stored server-side, so a stolen cookie can be revoked.
Rate limiting
Auth endpoints allow 20 attempts per IP per 15 minutes; the rest of the API allows 500.
Role hierarchy
requireRole("engineer") admits engineers and admins — permissions are inherited, never duplicated.
Org scoping
The organisation id comes from the verified token, never from the request body or query string.
WaterSim Pro
The Flows
12
Notes: Two tokens with different lifetimes is the design. Access token short and in memory; refresh token long, httpOnly, server-side and revocable. The table is the "why should I trust this" answer.

## Slide 13
FLOW 02
Building a flowsheet on the canvas
The canvas is the heart of the product — a live drawing sheet, not a static diagram.
1
Drop a unit
Pick from a palette of 26 unit operations grouped in nine categories. Each one arrives with sensible default parameters.
2
Wire the streams
Connect outlet to inlet. An edge carries a stream role, so the solver knows a RAS line from a WAS line from a permeate line.
3
Tune parameters
The parameter panel is generated from the unit model, so it only ever offers parameters the maths actually uses.
4
Save automatically
Three seconds after the last edit the canvas persists itself. Undo and redo are local and unlimited within a session.
5
Snapshot a version
Freeze the current canvas as a read-only snapshot — the "as tendered" or "as built" copy that later edits can never disturb.
ALWAYS LIVE
Symbols animate from real values, not decoration — flow, level and load drive the motion.
WHAT THE CANVAS GIVES YOU
Live readouts on every node
Info tips on every parameter
Presence avatars & remote cursors
Live charts dock
Alarm bell with active count
Dev FPS overlay
Undo / redo history
Preview runs that are never saved
WaterSim Pro
The Flows
13
Notes: The canvas is what people remember from a demo. Emphasise the last point in the navy box: the animation is driven by computed values, so a still screenshot of the canvas is already a data visualisation.

## Slide 14
THE LIBRARY
Twenty-six unit operations, nine categories
Each palette block maps to a process model that computes removal, sizing and energy.
Flow boundaries
Inlet (source) · Outlet (discharge)
Flow control
Pump · Valve
Preliminary
Screening · Grit removal
Primary
Primary clarifier
Secondary (biological)
Activated sludge · Secondary clarifier · Membrane bioreactor · UCT reactor (EBPR) · JHB reactor (EBPR) · Anaerobic digester
Tertiary
UV disinfection · Chlorination · Granular filter
Chemical dosing
Chemical dosing · Coagulant · Polymer · pH adjustment
Water purification
Coagulation / floc · RO membrane · UF membrane · GAC adsorption
Utilities
Blower · Storage tank
Behind the 26 blocks sit 15 process models — several palette blocks share a model (the three EBPR reactors all use the aeration-basin model with different recycle wiring).
WaterSim Pro
The Flows
14
Notes: Twenty-six palette blocks, fifteen models. Be honest about the mapping — several blocks share a model. The EBPR reactors differ in recycle wiring, not in the underlying biology model.

## Slide 15
FLOW 03
Inside a simulation run
What happens between pressing Run and seeing numbers on the canvas.
1
Validate
The request body is checked; oversized canvases are rejected before anything is created.
2
Create the run
A simulation_runs row is inserted with status "running". Previews are never recorded.
3
Resolve inputs
Node parameters, project cost overrides and the active permit template are merged.
4
Solve
A worker thread runs the solver: max 4 concurrent, 60-second limit, FIFO queue.
5
Cost & comply
Steady-state results are priced, then scored against the permit limits — pass or fail.
6
Persist & return
Results, costs, warnings and quality flags are stored and streamed to co-editors.
THREE WAYS TO RUN IT
Steady state
One converged operating point. Full cost breakdown and permit compliance. This is the default and the basis of every report.
Dynamic
The steady-state solver stepped through a 24-hour diurnal profile — flow and load scaled hour by hour, appropriate for slow biological processes.
Batch
A parameter sweep: the same flowsheet solved repeatedly across a range of inputs, recorded as a single run for comparison.
Safety net: a background reaper marks any run still "running" after 15 minutes as failed, so a crashed process can never leave a run hanging forever.
WaterSim Pro
The Flows
15
Notes: The important architectural point is step 4: the solver never runs on the event loop. One worker per run, four at a time, hard 60-second limit. The reaper at the bottom is the answer to "what if the process dies mid-run".

## Slide 16
FLOW 04
How the solver works
A flowsheet is a directed graph. Solving it is a topological walk — until a recycle loop makes that impossible.
Order the graph
Kahn's algorithm orders units by in-degree, so every unit is solved only after its feeds are known. Branch-and-merge networks solve in a single pass.
Find the real loops
Cycles are detected structurally. Only edges genuinely inside a cycle are torn — a feed-forward split-and-rejoin is never mistaken for a recycle.
Iterate to convergence
Torn RAS and WAS streams are solved by fixed-point iteration: up to 50 passes, tolerance 1e-4, with 0.5 relaxation damping when it starts to oscillate.
Report honestly
Unrouted side streams are warned about, not silently dropped. Non-finite values are swept to null and flag the run degraded.
WHAT EVERY RESULT CARRIES
converged
Did the fixed-point iteration reach tolerance?
iterations
How many passes it took.
maxResidual
The largest remaining imbalance.
degraded
Were any values unusable?
warnings[]
Everything the engine wants you to know.
The design principle: the engine would rather tell you it is unsure than quietly hand you a confident wrong number.
WaterSim Pro
The Flows
16
Notes: The technical heart. Kahn ordering for the DAG, structural cycle detection so only real recycles get torn, fixed-point iteration for those. The closing line is the design philosophy and worth landing slowly.

## Slide 17
FLOW 05
From mass balance to money
Cost is derived from the simulation, not typed in beside it — change a basin and the price moves with it.
OPERATING COST — FIVE CATEGORIES
Energy
Aeration from oxygen demand, UV lamps, RO feed pumps — less a biogas credit.
Chemicals
Aggregated from the actual dosing units on the canvas.
Sludge disposal
Thickened and dewatered biosolids at a tipping fee.
Labour
Parametric staffing by plant capacity.
Maintenance
A percentage of the modelled installed capital.
CAPITAL COST — SIZE-DRIVEN
direct cost = C₀ × ( S / S₀ ) ⁿ
The six-tenths rule (n ≈ 0.6–0.8), applied per unit to the size the model actually computed — clarifier area, basin volume, membrane capacity, lamp count, digester volume.
Installed cost
A Lang-type installation and indirects factor converts direct to installed.
Annualised
Capital recovery factor CRF = r(1+r)ⁿ / ((1+r)ⁿ − 1).
LCOW
Levelised cost of water = (annualised CAPEX + OPEX) ÷ annual treated volume.
COSTS ARE CONFIGURABLE AT THREE LEVELS
Engine defaults (2026 USD correlations)
beaten by
Project overrides (saved in project settings)
beaten by
Run overrides (sent with the request)
WaterSim Pro
The Flows
17
Notes: Cost is derived, never typed in beside the model. The six-tenths rule is standard engineering practice — the point is that S comes from what the unit model actually computed, so a bigger basin really does cost more. Three levels of override for when the defaults are wrong for a region.

## Slide 18
FLOW 06
Proving compliance with the discharge permit
The permit is configured once for the organisation, then applied automatically to every run.
1
Define the template
An engineer or admin creates a permit template holding the effluent limits: BOD, COD, TSS, total nitrogen, total phosphorus and the rest.
2
Activate one
Exactly one template is active per organisation at a time — enforced by a unique constraint, so there is never ambiguity about which limits applied.
3
Apply on every run
The active template is loaded server-side and passed into the solver. The engineer cannot forget it, and cannot quietly substitute different limits.
4
Score the effluent
Each limited parameter is compared to the modelled effluent. The run is marked compliant or not, and the specific violations are listed.
5
Record what was used
The run stores the limits it was judged against, so a report produced a year later still shows the permit in force at the time.
WHY IT MATTERS
Compliance becomes a property of the run, not a claim in a covering email.
AND WHERE THE VERDICT SHOWS UP
On the canvas
A pass or fail badge appears the moment a run returns.
In the reports list
Filter the run list by compliance to find every failing scenario.
In the PDF
A section lists each limit, the value and the margin.
As an alarm
A breached limit can raise an alarm event with its own history.
WaterSim Pro
The Flows
18
Notes: The strong claim is step 3: the permit is loaded server-side, so the engineer cannot forget it or quietly swap in friendlier limits. Step 5 is what makes an old report still defensible.

## Slide 19
FLOW 07
Reporting, export and comparison
Node.js builds the report data; Python renders it. Four audiences, four formats.
REPORTLAB + MATPLOTLIB
PDF report
An engineering document: flowsheet summary, stream table, unit results, removal efficiencies, cost breakdown, permit compliance and charts.
OPENPYXL
Excel workbook
A multi-sheet workbook for a single run, and a second layout for comparing runs — the format reviewers interrogate.
STREAMED
CSV export
Flat stream and event data for anyone who wants to do their own analysis without asking for an API key.
PURE JS LAYER
Plain language
A one-line verdict and a readable story for non-engineers — volumes compared to swimming pools and bathtubs, with a glossary.
AND AROUND THE EXPORTS
Report history
Every completed run across the organisation, filterable by project, mode and compliance.
Saved reports
Bookmark a run with a label and notes so a key scenario is never lost in the list.
Scenario comparison
Select two to six runs and compare effluent quality, removal efficiency and cost side by side.
Infinite scroll
The list pages by keyset cursor and renders virtually — it stays fast at any history size.
The Python renderers run in a hardened child process: interpreter pinned, 30-second timeout, 50 MB output cap and a shared concurrency limit.
WaterSim Pro
The Flows
19
Notes: Four formats for four audiences. The plain-language layer is the one people react to — a readable verdict with everyday comparisons, for the people who sign off but do not read mass balances.

## Slide 20
FLOW 08
Connecting the model to the real plant
A canvas parameter can be bound to a live PLC tag, so the simulation runs on what the plant is actually doing.
1
Define a connection
A PLC device: protocol, host, port, credentials. Test it before saving.
2
Bind tags to parameters
One binding maps one tag to one node parameter — read, or read-write.
3
The poller reads
A 500 ms scheduler reads each binding on its own interval, 2 s by default.
4
Values reach the canvas
Fresh samples broadcast to the flowsheet WebSocket room as plc:update.
5
Alarms evaluate
Every good sample is checked against the parameter alarm rules.
FIVE PROTOCOLS
Modbus TCP
Native Node, dependency-free over a raw socket.
Simulator
A built-in virtual PLC — no network, no hardware.
OPC UA
Python bridge via asyncua.
Siemens S7
Python bridge via python-snap7.
EtherNet/IP
Python bridge via pycomm3.
HOW IT STAYS HONEST
good
The read succeeded on this cycle.
bad
The device answered with a tag-level error — only that binding is affected.
stale
The connection is down. The last value is kept, but clearly marked as no longer current.
A lost connection triggers exponential backoff from 1 s up to 30 s — it never hammers a device that is already struggling.
WaterSim Pro
The Flows
20
Notes: This is what separates a design tool from an operations tool. Five protocols; two native in Node, three through a Python bridge because the mature clients live there. The quality flags on the right are the honesty story — a stale value is never presented as current.

## Slide 21
FLOW 09
Alarms — limits, breaches and history
A rule is a limit on something the flowsheet genuinely has. An event is what happened when that limit was crossed.
Rules are validated at creation
A rule can only point at a target the canvas actually exposes: a node parameter, a node output, or a value in the effluent summary. You cannot set a min/max on a deleted node, or on a text setting where a limit is meaningless.
Two evaluation sources
Rules are checked after each persisted simulation run, and against every good PLC sample as it arrives. Enabled parameter rules are cached per flowsheet for ten seconds, so the poller never pays a query per tick.
Events have a lifecycle
A new breach opens an active event and broadcasts "raised". A repeat breach only refreshes the value and timestamp. A clean evaluation flips the event to cleared. A later re-breach opens a new event, never reuses the old one.
THE EVENT STATE MACHINE
Clean
Breach detected
ACTIVE event
Evaluated clean
CLEARED
Re-breach → new event
WHERE ALARMS SURFACE
Alarm bell
A live count in the canvas header, updated over the WebSocket.
Alarms panel
Active and recent events for the flowsheet you are editing.
Alarms page
Organisation-wide event history, filterable and exportable to CSV.
PDF alarm report
A rendered event report for a review meeting or a regulator.
WaterSim Pro
The Flows
21
Notes: Two ideas. First, a rule can only target something the flowsheet actually has, validated at creation. Second, events have a real lifecycle rather than being a log line — raised, refreshed, cleared, and a re-breach opens a new event so the history stays truthful.

## Slide 22
FLOW 10
Real-time collaboration
A flowsheet is a room. Everyone editing it sees the same canvas change at the same moment.
1
Authorise the upgrade
The JWT is verified during the WebSocket handshake, then the flowsheet is traced up to its project and organisation before the upgrade completes.
2
Join the room
Rooms are keyed by flowsheet id. On joining, the client receives the full presence list; everyone else receives a presence update.
3
Broadcast the edits
Node adds, moves and deletes, edge changes, parameter updates and cursor movement all fan out to the other members of the room.
4
Share the results
Simulation start and completion are broadcast too — one person presses Run and everybody watches the numbers land.
THE MESSAGE VOCABULARY
presence:init
presence:update
cursor:move
node:add
node:move
node:delete
edge:add
edge:delete
params:update
sim:running
sim:result
plc:update
ONE DELIBERATE ASYMMETRY
Client messages are checked against an allowlist. "plc:update" is deliberately absent from it — only the server may emit live plant values, so a browser can never forge a reading from the plant.
WaterSim Pro
The Flows
22
Notes: Rooms keyed by flowsheet, authorised at the handshake. The asymmetry at the bottom is a deliberate security decision worth calling out: clients can send edits, but only the server can emit live plant values.

## Slide 23
PART 04
Engineering
The work that does not show up in a demo: speed, safety, proof and delivery.
Performance
Security
Testing & CI
Deployment & operations
WaterSim Pro
23
Notes: Transition. "The work that does not show up in a demo."

## Slide 24
ENGINEERING
Performance engineering
Three pressure points: a canvas with many nodes, a results list with many rows, and a solver that must never block the API.
The canvas
Hot handlers wrapped in useCallback so identity is stable
React.memo on edges and side panels — ReactFlow re-renders everything otherwise
Derived summary, costs and warnings computed with useMemo
Auto-save debounced to 3 s after the last edit
A dev-only FPS overlay, green above 55 fps, red below 30
The lists
A virtual-scroll hook renders only the visible rows
Fixed 56 px row height keeps the slice arithmetic O(1)
Sticky header, skeleton overlay while loading
Cursor pagination on completed_at instead of OFFSET
Infinite scroll via an IntersectionObserver sentinel
The server
The solver runs in worker threads, never on the event loop
Concurrency capped at 4 with a FIFO queue in front
60-second wall-clock timeout terminates a runaway worker
Six partial indexes, created CONCURRENTLY, on completed runs
limit+1 fetch detects the next page without a second count
The rule applied throughout: keep the number of things in the DOM and the number of rows crossing the wire proportional to what the user can actually see.
WaterSim Pro
Engineering
24
Notes: Three pressure points, three answers. The unifying rule is at the bottom — keep DOM nodes and wire rows proportional to what the user can see.

## Slide 25
ENGINEERING
Security posture
Defence in layers — the network edge, the request, the query and the record.
At the edge
Helmet with a strict Content-Security-Policy
HSTS with preload, production only
CORS locked to a configured origin, credentials allowed
trust proxy set so client IPs survive the load balancer
On the request
JWT bearer authentication, then hierarchical RBAC
express-validator on every mutating body and param
Rate limits: 500 per 15 min global, 20 per 15 min on auth
A correlation id on every request, logged end to end
On the data
Parameterised SQL everywhere — no string-built queries
Every read scoped by the organisation id from the token
bcrypt password hashes, stripped from all responses
Refresh tokens stored server-side and revocable
At startup and after
Production requires JWT_SECRET, DATABASE_URL and CORS_ORIGIN
JWT_SECRET must be at least 32 characters, or startup fails
Privileged actions written to an audit log
Errors returned generically; stack traces stay in the logs
WaterSim Pro
Engineering
25
Notes: Four layers. If asked for the single most important one, it is org scoping on the data layer — that is what makes multi-tenancy safe rather than merely intended.

## Slide 26
ENGINEERING
Testing and continuous delivery
Three levels of test, enforced coverage floors, and a pipeline that builds the images it deploys.
17 JEST SUITES
API tests
Auth, RBAC, projects, flowsheets, the solver graph, mass conservation, cost, PLC drivers, alarms, reliability and health.
22 VITEST FILES
UI tests
Auth context, the API client, canvas symbols, motion gating, reduced motion, live store, pagination, undo/redo and the alarm dialogs.
PLAYWRIGHT
End-to-end
A browser smoke run across the real application, driven by the same configuration CI uses.
COVERAGE FLOORS ENFORCED IN CI
61 %
Statements
48 %
Branches
58 %
Functions
63 %
Lines
THE PIPELINE
Lint
Unit tests
Coverage gate
E2E
Build images
Push to GHCR
Static analysis
ESLint across both workspaces with the React and hooks plugins; Prettier for formatting.
Determinism
The plain-language layer is pure — same input, same output, no dates, no randomness — so its tests are exact.
Conservation tests
A dedicated suite asserts that mass in equals mass out across the solved graph, including recycles.
WaterSim Pro
Engineering
26
Notes: Three levels of test with floors enforced in CI, so coverage cannot quietly erode. The conservation suite is the one to mention to a process engineer: it asserts mass in equals mass out across the solved graph, recycles included.

## Slide 27
ENGINEERING
Deployment and operations
Two supported production targets, both fed by the same images and the same migration discipline.
Docker Compose
1
Pull the pinned image tags
2
Run migrations to completion
3
Rolling update behind nginx
4
Health check the new containers
5
Roll back automatically if the check fails
Kubernetes
1
kubectl apply -k with kustomize overlays
2
Secrets from a template, never committed
3
A migration Job runs before every rollout
4
Liveness and readiness probes split apart
5
A nightly pg_dump CronJob for backups
RUNNING IT IN ANGER
/health
Readiness. Checks the database, with the result cached for five seconds so probe traffic cannot open a connection per hit.
/health/live
Liveness. Touches nothing — a database outage must never get healthy pods restarted.
/metrics
Prometheus: request duration histograms and simulation timings by mode and outcome. Cluster-internal only.
Runbooks
Documented procedures for deployment, rollback, backup and a rehearsed restore drill.
WaterSim Pro
Engineering
27
Notes: Two targets, same images, same migration discipline. The split between /health and /health/live is the detail worth explaining: liveness must never touch the database, or a database outage restarts healthy pods and makes the outage worse.

## Slide 28
SCALE
The platform by the numbers
Where the codebase stands today.
~46k
lines of application code
73
REST endpoints
16
database tables
26
unit operations
15
process models
12
application pages
8
schema migrations
5
PLC protocols
4
user roles
3
simulation modes
HOW IT WAS BUILT
Delivered in sessions
Sixteen completed sessions, each one documented in a state file that the next session picks up from.
Foundations first
Monorepo, schema, auth and RBAC before any feature — then the engine, then the canvas, then the extras.
Quality passes on purpose
Whole sessions given to UX polish, multi-tenancy, reporting and performance — not squeezed between features.
WaterSim Pro
Engineering
28
Notes: Scale slide — use it if someone asks "how big is this". The bottom table is the process story: foundations first, then features, with whole sessions spent on quality.

## Slide 29
WHAT IS NEXT
Roadmap
In flight now, and the candidates queued behind it.
IN PROGRESS
Alarms on the canvas
Limits on validated targets, an event history, CSV export and a PDF alarm report — with the alarm bell and panel wired into the flowsheet.
Canvas redesign
All 26 equipment symbols redrawn and made value-driven: a live store, motion tokens, animated streams and readouts on every node.
CANDIDATES
Notifications
Real-time toasts over the existing WebSocket, and email when a long run completes.
User preferences
Dark mode, SI or imperial units, timezone and layout density.
Comments & annotations
Threaded discussion pinned to a flowsheet node or a report figure.
Advanced simulation
Sensitivity analysis, Monte Carlo, and batch parameter sweeps.
Wider E2E coverage
Playwright journeys beyond the current smoke run.
Documentation site
Storybook for the component library, Docusaurus for the guides.
WaterSim Pro
Roadmap
29
Notes: In progress at the top, candidates below. Ask the room which of the candidates matters most to them — this is the natural place to take input.

## Slide 30
IN SUMMARY
One model, from the drawing sheet to the discharge permit.
The flowsheet you draw is the model that gets solved, the model that gets priced, the model that gets checked against the permit, and the model the plant streams live data back into. Nothing is re-keyed between those steps.
Draw
a plant on the canvas
Solve
the mass balance
Price
the design honestly
Prove
it meets the permit
WaterSim Pro
30
Notes: Land the one-sentence version: the flowsheet you draw is the model that gets solved, priced, checked and fed live data. Nothing is re-keyed between those steps. Then open for questions.